## Slide 1
GOLF
CONFIDENTIAL · OEM PARTNERSHIP PROPOSAL
Foldable Golf Shaft
Connection Mechanism
A play-grade, flush-profile collet compression joint
engineered for OEM shaft integration — travel-ready without compromise.
Preliminary Technical Review · February 2026 · Mechanical Engineering

## Slide 2
MARKET OPPORTUNITY
The Travel Problem No One Has Solved
Golf equipment travel is expensive, inconvenient, and antiquated — the market is waiting for a premium solution.
Shipping Cost
Checked golf bags cost $50–$150 each way with airlines. Ship Sticks and similar services charge $80–$200 per shipment. A week-long golf trip routinely adds $300–$500 in logistics cost.
Physical Bulk
A standard golf bag is 50"+ tall — it cannot fit in any checked luggage, carry-on, or standard vehicle trunk without a dedicated travel bag. Hotels charge storage fees. Taxis refuse them.
Damage Risk
Airline baggage handling breaks or bends shafts regularly. Replacement cost for a premium shaft set: $800–$3,000+. Travel cases add 15–25 lbs of dead weight to every trip.
$26B
annually
Est. US golf travel market
3.4
per year
Avg. trips per avid golfer
$150–500
USD avg.
Club shipping cost per trip
38%
to avoid logistics
Golfers who rent on trips

## Slide 3
SOLUTION OVERVIEW
A Two-Piece Shaft That Looks Like One
The IP is the connection mechanism — OEM shaft manufacturers install it. We own the joint.
GRIP HALF
COLLET JOINT
← YOUR IP →
HEAD HALF
Manufactured by OEM partner
(True Temper, Fujikura, Nippon, etc.)
Internal collet, mandrel,
sleeve, detent — proprietary
Manufactured by OEM partner
(same flex profile, same layup)
Flush Profile
Entire mechanism lives inside the shaft OD — zero visible collar
OEM Compatible
Sleeve installed at factory — no shaft redesign required
Play Grade
Collet compression delivers >150 Nm bending capacity

## Slide 4
PATENT LANDSCAPE
Prior Art — 13 Patents Reviewed
All major mechanisms are expired. The connection mechanism design space is open. Full patent table: bit.ly/golf-shaft-patents
Telescopic
Hesser (1998) most cited — OEM compatible approach, expired
4
Hinged
Training aids only — insufficient for play-grade ball-striking loads
5
Threaded
Simple but loosen under torsion — unsuitable for high-torque swing
2
Tapered Friction
Solid mechanism but protrudes beyond shaft OD — aesthetic failure
2
KEY FINDING: No prior patent addresses a flush-profile, tool-free, play-grade collet-based connection mechanism for golf shafts. Design space is open.

## Slide 5
MECHANISM SELECTION
Why Collet Compression Wins
Compared against four alternative joint concepts across six engineering criteria.
Criterion
Telescopic
Threaded
Bayonet
Hinged
Collet (Ours)
Flush OD Profile
✗
✗
✗
✓
✓
Bending Capacity
✓
✓
✓
✗
✓
Torsional Resistance
✓
✓
✓
✗
✓
Tool-Free Assembly
✓
✗
✓
✓
✓
USGA Conforming
~
~
~
✗
✓
OEM Compatible
✗
~
~
✓
✓
✓ Pass ~ Conditional ✗ Fail — Collet compression is the only mechanism meeting all six criteria simultaneously
CRITICAL DIFFERENTIATOR: All mechanism load transfer occurs inside the shaft bore — external OD is uninterrupted graphite tube at every point.

## Slide 6
TECHNICAL ARCHITECTURE
Component Breakdown
5 components — all housed within the shaft ID envelope. Nothing protrudes beyond the shaft OD.
01 Internal Sleeve (×2)
Ti-6Al-4V · 13.3mm OD / 10.5mm ID · 90mm long
02 Split Collet
17-4PH Stainless · 6 fingers · EDM-cut slots · TiN coated
03 Tapered Mandrel
Ti-6Al-4V · 8–10° half-angle · DLC coated · Ra 0.4μm
04 Detent Assembly
Inconel 718 spring · Si₃N₄ ceramic ball · ~200N release force
05 Dual Anti-Rotation Keys
Ti keyways · 180° apart · H7/h6 fit · ±0.5° alignment
KEY DIMENSIONS
Shaft OD (mid-section)
15.5 mm
Shaft ID (mid-section)
13.5 mm
Sleeve OD
13.3 mm
Sleeve ID
10.5 mm
Collet engagement
18 mm
Bond length (each)
45 mm
Mandrel taper angle
8–10°
Detent release force
~200 N
Added joint weight
~6–9 g
Thread spec (internal)
M11 × 1.0 fine
Interactive cross-section diagram available in the supplementary technical report: bit.ly/golf-shaft-collet

## Slide 7
ASSEMBLY SEQUENCE
Three States — Push to Lock
Tool-free assembly. Audible detent click confirms full engagement. Hard mechanical end-stop prevents incomplete assembly.
01
Separated
Two Independent Halves
Grip and head halves are independent structural tubes. Collet sits in relaxed (open) state inside grip-half sleeve bore, held captive by retaining lip. Bore caps protect internal surfaces during transport.
JOINT CAPACITY
0%
02
Engaging
Collet Contacts Mandrel Taper
Axial push brings halves together. Collet fingers enter head-half sleeve and contact the 8–10° mandrel taper. Fingers begin radial compression — friction preload builds progressively. Golfer feels increasing resistance.
JOINT CAPACITY
~45%
03
Locked
Full Engagement — Ready to Play
Collet fully seated on mandrel taper. Detent ball snaps into circumferential groove — audible click and tactile confirmation. Hard mechanical end-stop prevents over-travel. Load capacity: >150 Nm bending, >40 Nm torsion.
JOINT CAPACITY
~98%
→
→

## Slide 8
MATERIAL SPECIFICATION
Material Selection Rationale
Every material decision is driven by fatigue life, galvanic compatibility with graphite, and weight budget.
Internal Sleeve
Ti-6Al-4V
Galvanic compatibility with graphite, 1100 MPa UTS, excellent fatigue life. 4× cost vs Al but eliminates galvanic corrosion failure mode (FM-09) entirely.
Split Collet
17-4PH SS (H900)
Higher elastic compliance than Ti — fingers deflect adequately. 1310 MPa UTS, 620 MPa fatigue limit. EDM slot cutting + shot-peen essential.
Tapered Mandrel
Ti-6Al-4V
Matched CTE to sleeve — no differential thermal expansion at joint. DLC coating (3000+ HV) eliminates galling against collet TiN (FM-03).
Detent Spring
Inconel 718
Superior set-resistance vs. steel at elevated temperature (car boot 70–80°C). Rated to 650°C continuous — overkill, but ensures zero spring set over product life.
Detent Ball
Si₃N₄ Ceramic
Hardness 1500+ HV. Does not gall against titanium groove. 40% lighter than steel equivalent, reducing spring load required for same retention force.
Structural Adhesive
Hysol EA9394
35 MPa shear on composite-to-metal. Tg 121°C — covers worst-case summer storage. ~65,800 N theoretical shear capacity over 45mm bond length.
WEIGHT BUDGET: Total joint weight addition ~6–9g — less than a standard ferrule + grip cap. Swingweight compensation: trim 0.5" from grip-half butt end.

## Slide 9
FAILURE MODE & EFFECTS ANALYSIS
Risk Profile — 10 Failure Modes Identified
RPN = Severity × Occurrence × Detectability. Full interactive FMEA: bit.ly/golf-shaft-fmea
2
CRITICAL
RPN ≥ 200
3
HIGH
RPN 120–199
3
MEDIUM
RPN 60–119
2
LOW
RPN < 60
TOP FAILURE MODES BY RISK PRIORITY
FM-01
Adhesive Bond Peel
Catastrophic sleeve debond — progressive, externally invisible until failure
RPN 252
FM-02
Collet Finger Fatigue Fracture
High-cycle fatigue at slot root — sudden loss of preload
RPN 216
FM-03
Galling at Collet–Mandrel Interface
Ti-Ti cold welding — joint seizes permanently if uncoated
RPN 168
FM-04
Detent Spring Fatigue / Loss of Preload
Spring set reduces retention — joint can disengage under vibration
RPN 140
FM-05
Torsional Microslip
Fretting at friction interface — addressed by anti-rotation keyway
RPN 126

## Slide 10
RISK MITIGATION
Priority Design Actions
Six design decisions that collapse the FMEA risk profile from unacceptable to production-ready.
P1 · SAFETY CRITICAL
Tapered Sleeve Terminus
5–8mm chamfer on sleeve OD at both bond ends eliminates the stiffness step driving adhesive peel (FM-01) and bore ovality (FM-07). Zero cost penalty — one toolpath change.
P1 · SAFETY CRITICAL
Hard End-Stop + Loud Detent
Collet bottoms on machined shoulder — physically impossible to under-engage. Detent provides audible confirmation. Eliminates mid-swing separation risk (FM-08) entirely.
P2 · PERFORMANCE
EDM Slots + Shot-Peen
EDM cutting leaves compressive residual stress at slot roots. Shot-peen compounds benefit. Together: 3–5× fatigue life improvement over conventionally milled collet (FM-02).
P2 · PERFORMANCE
TiN + DLC Coating Pair
TiN on collet (2300 HV) + DLC on mandrel (3000+ HV). Dissimilar hard coatings eliminate galling (FM-03) and dramatically reduce fretting wear (FM-05). Low-temperature deposition — no distortion.
P2 · PERFORMANCE
Captive Bore Cap with Tether
Snap-on cap on each half bore. Internally tethered — cannot be lost. Eliminates contamination failure (FM-06). Premium branding surface — bears product mark. First thing golfer touches each round.
P3 · QUALITY
Dual Keyway (180° Apart)
Two keyways halve rotational backlash vs. single keyway for same tolerance. Doubles torsional mechanical capacity. Ensures ±0.5° graphic alignment at assembly (FM-10). One additional EDM pass.
Full failure timeline and test protocols available in the supplementary FMEA report: bit.ly/golf-shaft-fmea

## Slide 11
VALIDATION PROTOCOL
Test to Pass Before Production Commitment
7 test programs — structured to gate OEM partnership milestones. All methods reference established ASTM/industry standards.
T01
Assembly Cycle Fatigue
10,000 cycles
No finger fracture · Detent force >80N · Graphic align ±1°
FM-02, 04, 10
T02
Bending Fatigue
500,000 cycles @ 110 Nm
No adhesive crack >5mm · Bore ovality <0.1mm
FM-01, 07
T03
Torsional Capacity
Static torque to failure (3 specimens)
Slip torque >40 Nm · No surface damage
FM-05
T04
Thermal Cycling
-20°C to +80°C · 100 cycles
Bond strength retained >80% · Detent force within spec
FM-01, 04, 09
T05
Contamination Ingestion
ASTM G65 grit · 100 assemblies sans cap
Ra <0.8μm post-test · Torsional capacity >90%
FM-06
T06
Galvanic / Salt Fog
ASTM B117 · 500 hours assembled
No visible corrosion · Bond strength >85%
FM-09
T07
Drop / Impact
1.2m onto concrete grip-end · 10 drops
No joint separation · Detent engagement maintained
FM-01, 08
ID
Test Program
Method / Target
Pass Criterion
FM Ref

## Slide 12
PARTNERSHIP PROPOSAL
Next Steps & IP Strategy
A clean IP boundary between shaft manufacture and connection mechanism — your manufacturing expertise, our joint design.
IP BOUNDARY
OEM PARTNER
· Shaft layup schedule & flex profile
· Kick point location (determines cut position)
· Material sourcing & tube manufacture
· Quality control & tolerances
· Brand, finish, graphics
LICENSOR (US)
· Collet geometry & finger count
· Mandrel taper specification
· Dual anti-rotation keyway
· Detent mechanism design
· Sleeve tapered terminus geometry
DEVELOPMENT MILESTONES
Phase 1
Prototype & Proof of Concept · Months 1–3
Machine first collet/mandrel/sleeve set · Static load test to failure · Surface coating trials
Phase 2
OEM Integration · Months 4–6
Partner shaft selection · Sleeve installation process definition · Cut location per kick point
Phase 3
Validation Testing · Months 7–10
Run full 7-program test protocol · USGA conformance submission · Iterate on any failures
Phase 4
Production & Launch · Month 12+
Patent filing finalized · Manufacturing scale · Launch in premium travel golf market
SUPPLEMENTARY TECHNICAL REPORTS
Patent Landscape — 13 patents, links, mechanism analysis
→ Open Report
FMEA Report — 10 failure modes, RPN scores, test protocol
→ Open Report